## Slide 1: Cross-Core Prime+Probe Attacks on Non-inclusive Caches
Mengjia Yan, Read Sprabery, Bhargava Gopireddy,
Christopher Fletcher, Roy Campbell, Josep Torrellas
University of Illinois at Urbana-Champaign

## Slide 2: Modern Cache Hierarchies
Modern systems are moving to non-inclusive cache hierarchies
  Latest Intel server processor uses non-inclusive caches
Existing conflict-based attacks do not work on sliced non-inclusive caches
 | Skylake-S (Sep 2015) | Skylake-X/Skylake-SP (Jun 2017)
L2 | 256KB/core 16-way, inclusive | 1MB/core 16-way, inclusive
LLC | 2MB/core 16-way, inclusive | 1.375MB/core 11-way, non-inclusive
Core 0 | LLC Slice 0 | LLC Slice 4 | Core 4
Core 1 | LLC Slice 1 | LLC Slice 5 | Core 5
Core 2 | LLC Slice 2 | LLC Slice 6 | Core 6
Core 3 | LLC Slice 3 | LLC Slice 7 | Core 7

## Slide 3: Challenges of Prime+Probe Attacks
Lack of Visibility into the Victim’s Private Cache
target address
eviction addresses
victim
cache 0
attacker
cache 1
insert to LLC.
cache conflict.
evict an
inclusion
victim
(a) inclusive cache
insert to LLC.
No conflict
No inclusion victim
(b) non-inclusive cache
private
caches
shared
cache
Victim’s line duplicates in L1 and L2
Victim’s line does not exist in L2
eviction set (EV)
victim
cache 0
attacker
cache 1

## Slide 4: Challenges of Prime+Probe Attacks
Eviction Set Construction is Hard
target address
(a) inclusive cache
private
caches
shared
cache
slice 0
slice 1
slice 0
slice 1
(b) non-inclusive cache
eviction address
insert to shared cache
insert to private cache
evict to
shared cache
both evict to DRAM
also insert to private cache
Eviction is only determined by the LLC replacement policy.
Eviction is affected by the replacement policies in multiple caches, and address slice distributions.
Need LLC conflicts on the target slice to further evict the target line.

## Slide 5: Contributions
Previous attacks on inclusive caches are an example of directory attack.
We develop an algorithm to create Eviction Set on sliced non-inclusive caches.
We reverse engineer the directory structure in Intel Skylake-X processors.
We identify that directory as a unified structure to bootstrap conflict-based cache attacks for different cache hierarchies.
Based on our insights into the directory, we design the first Prime+Probe attack on sliced non-inclusive LLCs.

## Slide 6: The Inclusive Directory Structure
Attack opportunity analysis:
Insight: Directory must be inclusive to maintain tracking information for all the cache lines resident in the cache hierarchies.
 |  |  | …… |  | 
 |  |  | …… |  | 
 |  |  | …… |  | 
Extended
Directory
(ED)
Traditional
Directory
Directory and Tags
 |  |  | …… |  | 
 |  |  | …… |  | 
 |  |  | …… |  | 
Cache Lines
LLC Slice
 |  | …… |  | 
 |  | …… |  | 
 |  | …… |  | 
directory entry
for lines in LLC
directory entry
for lines in L2 but not LLC
The new attack surface!
Due to the associativity difference, we can create ED conflicts.
Can ED conflicts lead to inclusion victims?

## Slide 7: Creating Inclusion Victims via ED Conflicts
 |  | …… |  | 
 |  | …… |  | 
 |  | …… |  | 
 |  | …… |  | 
 |  | …… |  | 
 |  | …… |  | 
traditional
directory
 |  | …… |  | 
 |  | …… |  | 
victim
core 0
attacker
core 1
L2
extended
Directory
(ED)
cache lines
LLC
slice
target
address
 |  | …… | 
 |  | …… | 
 |  | …… | 
 |  | …… | 
 |  | …… | 
 |  | …… |  | 
 |  | …… |  | 
 |  | …… |  | 
 |  | …… |  | 
directories
 |  | …… | 
cache
line
directory
entry
insert into L2 and ED.
ED conflict.
evict the target line from remote L2 to LLC
inclusion victim
probe
addresses
Prime: access probe lines to occupy the target set in a ED slice

## Slide 8: Prime+Probe Attacks Targeting the Directory
Prime: access probe lines to occupy the target set in a ED slice
Wait: wait for the victim to perform an access
Probe: re-access the probe lines and measure access latency
 |  | …… |  | 
 |  | …… |  | 
 |  | …… |  | 
 |  | …… |  | 
 |  | …… |  | 
 |  | …… |  | 
traditional
directory
 |  | …… |  | 
 |  | …… |  | 
victim
core 0
attacker
core 1
L2
extended
Directory
(ED)
cache lines
LLC
slice
 |  | …… | 
 |  | …… | 
 |  | …… | 
 |  | …… | 
 |  | …… |  | 
 |  | …… |  | 
 |  | …… |  | 
 |  | …… |  | 
directories
victim does not perform access
 Probe latency is short
target
address
cache
line
directory
entry
probe
addresses

## Slide 9: Prime+Probe Attacks Targeting the Directory
Prime: access probe lines to occupy the target set in a ED slice
Wait: wait for the victim to perform an access
Probe: re-access the probe lines and measure access latency
 |  | …… |  | 
 |  | …… |  | 
 |  | …… |  | 
 |  | …… |  | 
 |  | …… |  | 
 |  | …… |  | 
traditional
directory
 |  | …… |  | 
 |  | …… |  | 
victim
core 0
attacker
core 1
L2
extended
Directory
(ED)
cache lines
LLC
slice
 |  | …… | 
 |  | …… | 
 |  | …… | 
 |  | …… | 
 |  | …… |  | 
 |  | …… |  | 
 |  | …… |  | 
 |  | …… |  | 
directories
① victim accesses target line
②directory entry migration. ED conflict.
Victim performs access  Probe latency is higher
target
address
cache
line
directory
entry
probe
addresses

## Slide 10: Conclusion
Directory = The unified structure for conflict-based cache attacks
“Attack Directories, Not Caches: Side-Channel Attacks in a Non-Inclusive World” recently accepted in IEEE Symposium on Security and Privacy (SP’19).
More in the Paper
Eviction set construction algorithm.
Steps of reverse engineering the directory structure.
Root cause analysis of the the vulnerability
A multi-threaded high-bandwidth Evict+Reload attack.
Attack results on AMD machines.